## Slide 1: Systems Architecture and Trajectory Optimization for High Thrust Interplanetary Spacecraft
Erik Payton and Prof. Mason Peck
Cornell University
AIAA Region 1 Student Conference
March 2023
Notes: Name and Introduction...you got this!!!

## Slide 2: Turn and Burn: Research Question
Current Interplanetary Travel
  Hohmann Transfer
    Minimum Fuel Trajectory
    170-200 day trip to Mars
Image Credit: SatNow
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview

## Slide 3: Turn and Burn: Research Question
Current Interplanetary Travel
  Hohmann Transfer
    Minimum Fuel Trajectory
    170-200 day trip to Mars
What about Minimum Time Trajectory?
  Not Practical with current technologies
  Trying to find what this looks like
Image Credit: SatNow
?
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview

## Slide 4: Turn and Burn: Research Question
Current Interplanetary Travel
  Hohmann Transfer
    Minimum Fuel Trajectory
    170-200 day trip to Mars
What about Minimum Time Trajectory?
  Not Practical with current technologies
  Trying to find what this looks like
Image Credit: SatNow
?
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
What does an Interplanetary Minimum-Time Trajectory look like?

## Slide 5: Turn and Burn: Maneuver Basics
Goal: Continuous High-Thrust Maneuver for Interplanetary Travel
  Hamilton-Jacobi-Bellman time optimality
  Future Propulsion Technologies
    Positron Induced Fusion Space Propulsion [3]
      Specific Impulse: 82,000 seconds
Half Period of Cosine Function as Motivation for the Maneuver
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview

## Slide 6: Turn and Burn: Maneuver Basics
Goal: Continuous High-Thrust Maneuver for Interplanetary Travel
  Hamilton-Jacobi-Bellman time optimality
  Future Propulsion Technologies
    Positron Induced Fusion Space Propulsion [3]
      Specific Impulse: 82,000 seconds
Half Period of Cosine Function as Motivation for the Maneuver
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
Assume Futuristic Propulsion to achieve Hamilton-Jacobi-Bellman time optimality.

## Slide 7: Further Considerations
This Paper: Orbital Mechanics and Mission Planning
Other areas of interest
  Structure: loads during maneuver
  Thermal: performance limitations
  Communications: Doppler Shift
  Relativistic Effects: 5% speed of light
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview

## Slide 8: Research Overview
Earth to Mars Case Study Results
  Methods of Simulation
Results with differing thrust levels
  3 different thrust levels
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
Earth Orbit
Mars Orbit
Close up of Mars Orbit Approach

## Slide 9: Research Overview
Earth to Mars Case Study Results
  Methods of Simulation
Results with differing thrust levels
  3 different thrust levels
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
Earth Orbit
Mars Orbit
Close up of Mars Orbit Approach
Examine a Case Study from Earth to Mars under 3 different Thrust levels.

## Slide 10: Overview of Assumptions
Spacecraft has 15000kg mass
  1/3 devoted to propellant
Orbit Eccentricities of 0
Destination is orbit rather than Planet
Very good approximation
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview

## Slide 11: Earth to Mars Case Study: Simulation
Simulated with MATLAB and Simulink
Optimal Trajectory
  Fminsearch
  Set of coefficients for the Thrust vector
  Optimal Flip Time
Cost function
  Weighted terms
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
= position of spacecraft
= position of desired orbit (mars)
es = eccentricity of spacecraft
em = eccentricity of desired orbit (mars)
= cost function value
= time required for the maneuver

## Slide 12: Earth to Mars Case Study: Simulation
Simulated with MATLAB and Simulink
Optimal Trajectory
  Fminsearch
  Set of coefficients for the Thrust vector
  Optimal Flip Time
Thrust Vector
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
= true anomaly angle
= thrust polynomial used in vector calcualtion
= thrust direction unit vector

## Slide 13: Earth to Mars Case Study: Simulation
Simulated with MATLAB and Simulink
Optimal Trajectory
  Fminsearch
  Set of coefficients for the Thrust vector
  Optimal Flip Time
Thrust Vector
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
= true anomaly angle
= thrust polynomial used in vector calcualtion
= thrust direction unit vector
Use Simulation to evaluate and Optimize Trajectory

## Slide 14: Earth to Mars Case Study: Results
Thrust to Provide 3g initial acceleration
Key Numbers
  Max Speed: 1680000m/s
  Thrust 441,000 N
  Total Maneuver Duration: 26.1 hours
  Flip Time: 14.3 hours (55%)
  Range of Thruster Angle: 0.0076 Rad
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
Earth Orbit
Mars Orbit

## Slide 15: Earth to Mars Case Study: Results
Thrust to Provide 3g initial acceleration
Key Numbers
  Max Speed: 1680000m/s
  Thrust 441,000 N
  Total Maneuver Duration: 26.1 hours
  Flip Time: 14.3 hours (55%)
  Range of Thruster Angle: 0.0076 Rad
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
Earth Orbit
Mars Orbit
Turn and Burn Trajectory provides much faster travel times.

## Slide 16: Earth to Mars Case Study: Results
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview

## Slide 17: Earth to Mars Case Study: Results
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview

## Slide 18: Earth to Mars Case Study: Other Thrusts
Examine Turn and Burn Maneuver under different Thrust levels
  3g initial acceleration
  1g initial acceleration
  0.5g initial acceleration
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
Earth Orbit
Mars Orbit

## Slide 19: Earth to Mars Case Study: Other Thrusts
Examine Turn and Burn Maneuver under different Thrust levels
  3g initial acceleration
  1g initial acceleration
  0.5g initial acceleration
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
Earth Orbit
Mars Orbit
Test validity of Turn and Burn in different conditions.

## Slide 20: Earth to Mars Case Study: Other Thrusts
 | 0.5 g Initial Accel | 1 g Initial Accel | 3 g Initial Accel
Max Speed | 679,000 m/s | 960,000 m/s | 1,680,000 m/s
Thrust | 74,000 N | 147,000 N | 441,000 N
Mission Duration | 64.3 hours | 45.5 hours | 26.1 hours
Flip Time | 35.1 hours | 24.83 hours | 14.34 hours
Range of Thruster Angle | 0.018 rad | 0.013 rad | 0.0076 rad
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview

## Slide 21: Earth to Mars Case Study: Other Thrusts
 | 0.5 g Initial Accel | 1 g Initial Accel | 3 g Initial Accel
Max Speed | 679,000 m/s | 960,000 m/s | 1,680,000 m/s
Thrust | 74,000 N | 147,000 N | 441,000 N
Mission Duration | 64.3 hours | 45.5 hours | 26.1 hours
Flip Time | 35.1 hours | 24.83 hours | 14.34 hours
Range of Thruster Angle | 0.018 rad | 0.013 rad | 0.0076 rad
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
Turn and Burn still has significant benefits at lower thrust.

## Slide 22: Earth to Mars Case Study: Other Thrusts
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview

## Slide 23: Earth to Mars Case Study: Other Thrusts
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview

## Slide 24: Conclusions and Current Status
Lay out framework for future technologies
Shorter Travel Times
  Less living requirements onboard
Further Research
  Subsystems of the Spacecraft
  Lunar Case with Nuclear Thermal Propulsion
Conclusions and Further Research
Trajectory with Different Thrust
Earth to Mars Case Study
Presentation Overview
Earth Orbit
Mars Orbit

## Slide 25: Acknowledgments and References
Acknowledgments
The research presented in this paper was conducted at Cornell University as a part of the Space Systems Design Studio. We would like to acknowledge Tina Daniel and Isaac Beaton for their work on other aspects of the Turn-and-Burn Project. Their work has helped confirm and expand upon the work presented in this paper.
References
[1] Drake, B. G. et al. “Human Exploration of Mars, Design Reference Architecture 5.0.” NASA Johnson Space Center 2009. [2] Kirk D. E., Optimal Control Theory An Introduction, Dover Publications, Inc. New York, 1998, Parts, I, IV [3] LeMoyne, R. “Positron Induced Fusion Pulsed Space Propulsion through an Ultra-Intense Laser.” Journal of Applied Mathematics and Physics, Vol.5, No.4, 2017. [4] “Space Shuttle News Reference” NASA 1981. [5] Daniel T, “Turn and Burn End of Semester Report (Cornell University Internal Document)” Cornell University, Ithaca, New York, 2022. (unpublished) [6] MATLAB and Simulink, Ver R2022b, Math Works, Natick, MA, 2022.

## Slide 26: Turn and Burn Interplanetary Maneuver
Questions?