## Slide 1: Optimal Cislunar Trajectories with Continuous, High-Thrust Nuclear-Thermal Propulsion
Erik Payton, Colby Merrill, Mason Peck, and Dmitry Savransky
Cornell University
January 6th, 2025
Notes: Name and Introduction...you got this!!!

## Slide 2: Outline
Background & Motivation
Research Methods
Case Study Results
Conclusion

## Slide 3: Outline
Background & Motivation
  Propulsion and Trajectories
  Minimum Time Transfers
  NTP Overview
Research Methods
Case Study Results
Conclusion

## Slide 4: Background
Propulsion Systems
  Chemical Propulsion: High Thrust, Low Isp
  Electric Propulsion: Low Thrust, High Isp
Cis-lunar Trajectories
  Lunar Free Return Trajectory
  Impulsive Maneuvers
  efficient trajectories
Notes: 1) Prop systems
- What is Isp
- Chemical
- Electric
2) Cis-Lunar Trajectories
- We want minimum fuel trajectories
- Impulsive (Hohmann Transfer)
- Lunar Free Return -- Apollo
What if we didn't care about these... :)

## Slide 5: Background: Minimum Time Trajectories
“Turn and Burn” Trajectory
  Minimize the Time-of-Flight Maneuver
  Satisfies Hamilton-Jacobi-Bellman Time optimality
  Continuous-High-Thrust Maneuver
  Not feasible outright with current technologies
[1] Clarke, Arthur C. The Songs of Distant Earth. New York: Del Rey Books, 1986.
[1]
Notes: Now we have a min time...aka turn and burn
1) Songs of Distant Earth
- Journey of the spaceship Magellan
- It uses a similar type of Maneuver
2) What does a Min time mean:
- Satisfies the Hamilton Jacobi Bellman time optimality
- Fastest transit method = accel then decell
- Current Tech is too limited in the Isp-Thrust space to capitalize on the major benefits of this type of maneuver

## Slide 6: Background: NTP Technology
Nuclear Thermal Propulsion
  Expand a working fluid (e.g. Hydrogen) using a small fission reactor
  800s – 1000s Isp
  Two large pitfalls
    Larger Engine Mass
    Non-negligible ramp times
Specification | NTP | Chemical
Thrust Class | 66,700 N | 66,700 N
Isp | 900 s | 451 s
Total Engine Mass | 4550 kg | 510 kg
Total Engine Length | 5.0 m | 2.3 m
Total Engine Diameter | 1.9 m | 1.9 m
[2] Harnack, C., Grella, E., Greenhalge, S., and Duchek, M., “Capabilities of Sinlge Launch NTP and Chemical Spacecrafts for Cis-Lunar Tug Missions,” Nuclear and Emerging Technologies for Space, 2023.
[2]
Notes: 1) NTP offers a new "middle of the road" technology
- High thrust capabilities
- High (ish) Isp
- How it works
2) What are the pitfalls
- Engine mass: The thrust per mass is much lower than chemical systems
- Non-neglagible ramps on the second slide--after some background

## Slide 7: Motivation: NTP and Turn and Burn
No ramp time hinderance on efficiencies
Continuous Thrust would require less thrust magnitude so the engine would be smaller, reducing mass
  NASA Artemis System [4]
    26.6 kN Thrust (Service Module)
    ~15,000 kg Mass (Service Module)
  Cont. Thrust
    300-400 N Thrust
    20,000 kg Spacecraft
    98% Decrease in thrust compared to Impulsive
    15-20% Increase in Isp Compared to NTP impulsive
[3] Duchek, M. E., Nikitaeva, D., Harnack, C., Grella, E., and Greenhalge, S., “Parametric Modeling of NTP Engine Performance for a Crewed Mars Mission,” ASCEND 2023, 2023.
[4] Bowman, A., Peters, E., “Orion Components”, NASA 2024
[3]
Notes: 1) Ramp inefficiencies
- order 200 s ramp times
- in an impulsive operational paradigm, avg is not the same as peak
2) What Continuous Thrust
- If continuously burning, smaller engine mass needed
- good considering the high mass cost
- Scaling information in backup
- the ramp times become negligible and avg approaches peak

## Slide 8: Outline
Background & Motivation
Research Methods
  Assumptions
  Dynamics
  Numerical Methods
Case Study Results
Conclusion

## Slide 9: Assumptions
Spacecraft considered in the Earth-Moon system
  Spacecraft Parameters
    Specific Impulse: 1000s
    Wet Mass: 20,000 kg
    Propellent Mass: 9,000 kg
  Orbital Parameters
    Starting Orbit: GEO
    Target Lunar Orbit: LLO
    1 DU = 384,400 km (amoon)
Moon
Earth
Spacecraft
Notes: Located in the Earth-Moon system
1) Spacecraft Parameters
2) Orbital parameters
3) Diagram - note the 3 vector quantities

## Slide 10: Dynamics
Gravitational interactions with Earth and Moon
Ephemeris Model
Force from propulsion system aligned with velocity vector
Earth Dynamics Lunar Dynamics Thrust
For Numerical Stability at Zero Velocity
Maneuver Flip time
Notes: 1) Modeling
- 3 accelerating terms: Earth, Moon, Propulsion system
- Ephemeris Model, using NAIF's Spice (Mice) package
2) Equation
- first 2 are standard newton gravity
- Thrust: fires along velocity direction, flip at tau_m
- 0.2 for numerical stability
3) Plot
- Magnitude plot
- Earth and moon domination sections
- Vertical flip time marking

## Slide 11: Numerical Methods
Adams-Bashforth-Moulton predictor-evaluator-corrector-evaluator solver
  Max/Min orders of 13 and 1
  Tolerances of 1 x 10−11
Nelder-Mead simplex algorithms described in [5] Lagarias et al, 1998
  Optimality achieved by minimizing the cost function
Integrated Time Boundary Value Problem: Radial Position Boundary Value Problem: Eccentricity
Notes: 1) Discuss the Set-Up
- Numerical Propagation of Dynamics wrapped in Optimizer
2) Cost Function
- BREIF overview
- Integrated term
- BVP Terms
- Sigmoid

## Slide 12: Outline
Background & Motivation
Research Methods
Case Study Results
Conclusion

## Slide 13: Results
Case Study I
  Exhaust Propellent
    Utilize all the propellent mass
    300 N to 410 N test range
  Parameters of Interest
    Flight time
    Normalized flip time
    Final eccentricity
  Continuation Analysis
    Use optimal results from last thrust level as an initial guess for the next
Case Study II
  Halt Integration at threshold
    Halt integration when eccentricity = 0.6
    300 N to 410 N test range
    Eccentricity should be constant
  Parameters of Interest
    Flight time
    Normalized flip time
    and Propellent exhausted
  “Continuation Analysis”
    Use corresponding result from case study I to inform guess for case study II
Notes: Both)
- Talk about the main goals
- Parameters of Interest
- Continuation Analysis

## Slide 14: Trajectory Bounds
Case Study 1
Case Study 2
Notes: Leading Edge Flybys

## Slide 15: Time of Flight
Case Study 1
Case Study 2
Notes: 1) Discuss how TOF is calculated in both cases
- Deterministic in C.S I

## Slide 16: Flip Time Percentage
Case Study 1
Case Study 2
Notes: 1) Talk abt the theoretical first, aka 50% to >50%
2) Linear
- Helpful in local estimations
3) CS II
- Not linear bc of undeterministic TOF

## Slide 17: Maneuver ∆V
Case Study 1
Case Study 2

## Slide 18: Results
Key Results
  Trajectories
    Max thrust from tested range achieves shorter TOF than Lunar free return
    about twice lunar free return
    Linear trends locally in for Case Study I
  Engine Mass
    Linear Scaling says order 20 kg engine mass
    Would not really be linear  motivates engine would be much smaller
Moon
Earth
Spacecraft

## Slide 19: Conclusion
Turn and Burn offers a new operational paradigm for NTP technology
The inherent benefits of running the reactor continuously could also include providing more power to the other systems of the spacecraft.
Order of magnitude smaller NTP engine
Erik D. Payton
edp48@cornell.edu
References
[1] Clark, A. C., 1986
[2] Harnack, C , 2023.
[3] Duchek, M. E., 2023.
[4] Bowman, A., 2024
[5]Lagarias et al, 1998

## Slide 20: Final Eccentricity
Case Study 1
Case Study 2

## Slide 21: Propellent Mass Consumption
Case Study 1
Case Study 2

## Slide 22: Backup
Analytical Expressions for Turn and Burn Maneuver
Hur, D., “Turn and Burn Closed Form Report (Cornell University internal document),” , 2023.

## Slide 23: Backup

## Slide 24: Backup: Engine Mass Scaling
Constant of Specific Technology
Want half of this
Must also be halved
Constants of these Equations:
All Stagnation Properties
Mach Number
RHS of all Equations is constant, given constant stagnation properties, and will be constant as well
Constant Ratio

## Slide 25: Backup: Engine Mass Scaling
Know this is halved
Must also be halved
Hoop Stress will be constant

## Slide 26: Backup: Engine Mass Scaling
With both t and r* scaling as the whole volume and therefore mass is simply halved, thus implying a simple linear scaling
Cylindrical Shell Volume formula
Notes: 1/rt(2)*(1/rt(2) = ½ means linaer

## Slide 27: Backup
Final Conditions:
a: 9.05e6 km
e: 0.472
Omega: 0 rad
I: 0 rad
omega: 0.5281 rad
Notes: 1/rt(2)*(1/rt(2) = ½ means linaer